## Slide 1
Chapter 2 Application Layer
Notes: Version History
8.1. Updates throughout, including a lot more animations. These are the ppt files used to make Chapter 2 online lectures in Sept. 2020.
8.0 (April 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout

## Slide 2: Application layer: overview
Principles of network applications
Web and HTTP

## Slide 3: Some network apps
social networking
Web
text messaging
e-mail
multi-user network games
streaming stored video (YouTube, Hulu, Netflix)
P2P file sharing
voice over IP (e.g., Skype)
real-time video conferencing (e.g., Zoom)
Internet search
remote login

## Slide 4: Application layer
This layer allows people to use the Internet
Other 4 layers are just made so people can use application programs

## Slide 5: Internet applications
Application | Application layer protocol | Transport protocol
E-mail | SMTP | TCP
Remote terminal access | telnet | TCP
Web | HTTP | TCP
File transfer | FTP | TCP
Streaming multimedia | Proprietary | TCP or UDP
Internet telephony | Proprietary | Typically UDP

## Slide 6: Application layer

## Slide 7: Creating a network app
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
write programs that:
run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
no need to write software for network-core devices
network-core devices do not run user applications
applications on end systems allows for rapid app development, propagation

## Slide 8: Application Architecture
Client-server Architecture
Peer to peer Architecture

## Slide 9: Client-server architecture
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
server:
always-on host
permanent IP address
often in data centers, for scaling
clients:
contact, communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other
examples: HTTP, IMAP, FTP

## Slide 10: Peer-peer architecture
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
no always-on server
arbitrary end systems directly communicate
peers request service from other peers, provide service in return to other peers
  self scalability – new peers bring new service capacity, as well as new service demands
peers are intermittently connected and change IP addresses
  complex management
example: P2P file sharing [BitTorrent]

## Slide 11: Processes communicating
process: program running within a host
within same host, two processes communicate using inter-process communication (defined by OS)
processes in different hosts communicate by exchanging messages
note: applications with P2P architectures have client processes & server processes
client process: process that initiates communication
server process: process that waits to be contacted
clients, servers

## Slide 12: Sockets
process sends/receives messages to/from its socket
socket analogous to door
  sending process shoves message out door
  sending process relies on transport infrastructure on other side of door to deliver message to socket at receiving process
  two sockets involved: one on each side
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 13: Ports
A numerical identifier (0–65535) used to distinguish different services on the same IP address.
Example: Port 80 for HTTP, Port 443 for HTTPS.
Think of it like an apartment number inside a building (the IP address is the building’s street address).

## Slide 14: Sockets
A combination of
  IP Address
  Port Number
  Protocol (TCP/UDP)
This uniquely identifies one endpoint of a network connections message out door
Example
  192.168.1.10:443 over TCP is one socket

## Slide 15: Addressing processes
to receive messages, process must have identifier
host device has unique 32-bit IP address
Q: does IP address of host on which process runs suffice for identifying the process?
identifier includes both IP address and port numbers associated with process on host.
example port numbers:
  HTTP server: 80
  mail server: 25
to send HTTP message to gaia.cs.umass.edu web server:
  IP address: 128.119.245.12
  port number: 80
more shortly…
  A: no, many processes can be running on same host

## Slide 16: An application-layer protocol defines:
types of messages exchanged,
  e.g., request, response
message syntax:
  what fields in messages & how fields are delineated
message semantics
  meaning of information in fields
rules for when and how processes send & respond to messages
open protocols:
defined in RFCs, everyone has access to protocol definition
allows for interoperability
e.g., HTTP, SMTP
proprietary protocols:
e.g., Skype, Zoom

## Slide 17: What transport service does an app need?
data integrity
some apps (e.g., file transfer, web transactions) require 100% reliable data transfer
other apps (e.g., audio) can tolerate some loss
timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
security
encryption, data integrity, …

## Slide 18: Transport service requirements: common apps
application
file transfer/download
e-mail
Web documents
real-time audio/video
streaming audio/video
interactive games
text messaging
data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
throughput
elastic
elastic
elastic
audio: 5Kbps-1Mbps
video:10Kbps-5Mbps
same as above
Kbps+
elastic
time sensitive?
no
no
no
yes, 10’s msec
yes, few secs
yes, 10’s msec
yes and no

## Slide 19: Internet transport protocols services
TCP service:
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
connection-oriented: setup required between client and server processes
does not provide: timing, minimum throughput guarantee, security
UDP service:
unreliable data transfer between sending and receiving process
does not provide: reliability, flow control, congestion control, timing, throughput guarantee, security, or connection setup.
Q: why bother? Why is there a UDP?

## Slide 20: Internet applications, and transport protocols
application
file transfer/download
e-mail
Web documents
Internet telephony
streaming audio/video
interactive games
application
layer protocol
FTP [RFC 959]
SMTP [RFC 5321]
HTTP [RFC 7230, 9110]
SIP [RFC 3261], RTP [RFC 3550], or proprietary HTTP [RFC 7230], DASH
WOW, FPS (proprietary)
transport protocol
TCP
TCP
TCP
TCP or UDP
TCP
UDP or TCP

## Slide 21: Securing TCP
Vanilla TCP & UDP sockets:
no encryption
cleartext passwords sent into socket traverse Internet in cleartext (!)
Transport Layer Security (TLS)
provides encrypted TCP connections
data integrity
end-point authentication
TLS implemented in application layer
apps use TLS libraries, that use TCP in turn
  cleartext sent into “socket” traverse Internet encrypted
  more: Chapter 8

## Slide 22: Application layer: overview
Principles of network applications
Web and HTTP

## Slide 23: WWW
World Wide Web
Introduced in 1991
originated from the CERN High-Energy Physics laboratories in Geneva, Switzerland.

## Slide 24: The Web: Some Jargon
Web page
  consists of objects (HTML file, JPEG image, GIF image…)
  addressed by URL
Most Web pages consist of
  base HTML page
  several referenced objects
URL
  A standard way of specifying the location of an object, typically a web page, on the Internet
User agent for Web is called a browser
  MS Internet Explorer
Server for Web is called a Web server

## Slide 25: HyperText Transfer Protocol
Web’s application layer protocol
  Used to access data on the World Wide Web
  Rapid jump from one document to another
Client-server model
  client: browser that requests, receives, “displays” web objects
  server: Web server sends objects in response to request
uses one TCP connection on the well-known port 80

## Slide 26: Web and HTTP
web page consists of objects, each of which can be stored on different Web servers
object can be HTML file, JPEG image, Java applet, audio file,…
web page consists of base HTML-file which includes several referenced objects, each addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 27: URL - continued
method
  protocol used to retrieve the document (FTP, HTTP, …)
host
  a computer where the info is located
  the name of the computer can be an alias (not necessary www)
port
  optional port # of the server
path
  the path name of the file where the info is located

## Slide 28
Figure 27.1 Architecture of WWW

## Slide 29: HTTP overview
HTTP: hypertext transfer protocol
Web’s application-layer protocol
client/server model:
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
HTTP request
HTTP response
HTTP request
HTTP response
iPhone running
Safari browser
PC running
Firefox browser
server running
Apache Web
server

## Slide 30: HTTP overview (continued)
HTTP uses TCP:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 31: HTTP connections: two types
Non-persistent HTTP
TCP connection opened
at most one object sent over TCP connection
TCP connection closed
downloading multiple objects required multiple connections
Persistent HTTP
TCP connection opened to a server
multiple objects can be sent over single TCP connection between client, and that server
TCP connection closed

## Slide 32: Non-persistent HTTP: example
User enters URL:
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80 “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(containing text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index

## Slide 33: Non-persistent HTTP: example (cont.)
User enters URL:
(containing text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index
5. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.
time

## Slide 34: Non-persistent HTTP: response time
RTT (definition): time for a small packet to travel from client to server and back
HTTP response time (per object):
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
object/file transmission time
time to
transmit
file
initiate TCP
connection
RTT
request file
RTT
file received
time
time
Non-persistent HTTP response time = 2RTT+ file transmission time

## Slide 35: Persistent HTTP (HTTP 1.1)
Non-persistent HTTP issues:
requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open multiple parallel TCP connections to fetch referenced objects in parallel
Persistent HTTP (HTTP1.1):
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects (cutting response time in half)

## Slide 36: Pipelining
Issue multiple requests at a time
  Don’t have to wait for previous response
  More efficient use of link
Use carefully
  POST requests should not be pipelined (changes server state)
  GET/HEAD requests are usually okay
Notes: Can put several requests in a single packet

## Slide 37: Persistent HTTP
Non-persistent HTTP issues:
Connection setup for each request
But browsers often open parallel connections
Persistent HTTP:
Server leaves connection open after sending response
Subsequent HTTP messages between same client/server are sent over connection
Persistent without pipelining:
Client issues new request only when previous response has been received
One RTT for each object
Persistent with pipelining:
Default in HTTP/1.1 spec
Client sends multiple requests
As little as one RTT for all the referenced objects
Server must handle responses in same order as requests

## Slide 38: “Persistent without pipelining” most common
When does pipelining work best?
  Small objects, equal time to serve each object
  Small because pipelining simply removes additional RTT delay to request new content
Notes: Head-of-line blocking: if big item is the first request, smaller requests are stuck waiting behind it to finish when they could be issued as a parallel connection

## Slide 39: HTTP protocol – message format
two types of messages: request & response
  ASCII (human-readable format)

## Slide 40: HTTP protocol – message format
HTTP request message
HTTP 0.9 HTTP 1.0 HTTP 1.1
GET – when the client wants to retrieve a document from the server
HEAD – when the client wants some info about a document but not document itself
COPY – copies the file to another location

## Slide 41: Method Types
HTTP/1.0:
GET
POST
HEAD
  asks server to leave requested object out of response
  i.e. request info about a doc
HTTP/1.1:
GET, POST, HEAD
PUT
  uploads file in entity body to path specified in URL field
DELETE
  deletes file specified in the URL field

## Slide 42: HTTP protocol – message format
HTTP response message
http://www.w3.org/Protocols/HTTP/HTRESP.html
explains the status code
in text form
200 OK – request succeeded
301 Moved Permanently – object moved
400 Bad Request – not understood by server
404 Not Found – req. document not found

## Slide 43: HTTP messages – an example
This example retrieves a document.
We use the GET method to retrieve an image with the path/usr/bin/image1.
The request line shows the method (GET), the URL, and the HTTP version (1.1).
The header has two lines that show that the client can accept images in GIF and JPEG format.

## Slide 44: HTTP response status codes
status code appears in 1st line in server-to-client response message.
some sample codes:

## Slide 45
HTTP response status codes

## Slide 46: Other HTTP request messages
POST method:
web page often includes form input
user input sent from client to server in entity body of HTTP POST request message
GET method (for sending data to server):
include user data in URL field of HTTP GET request message (following a ‘?’):
www.somesite.com/animalsearch?monkeys&banana
HEAD method:
requests headers (only) that would be returned if specified URL were requested with an HTTP GET method.
PUT method:
uploads new file (object) to server
completely replaces file that exists at specified URL with content in entity body of POST HTTP request message

## Slide 47: Trying out HTTP (client side) for yourself
1. netcat to your favorite Web server:
opens TCP connection to port 80 (default HTTP server port) at gaia.cs.umass.edu.
anything typed in will be sent to port 80 at gaia.cs.umass.edu
3. look at response message sent by HTTP server!
(or use Wireshark to look at captured HTTP request/response)
2. type in a GET HTTP request:
GET /kurose_ross/interactive/index.php HTTP/1.1
Host: gaia.cs.umass.edu
by typing this in (hit carriage return twice), you send this minimal (but complete) GET request to HTTP server
% nc -c -v gaia.cs.umass.edu 80 (for Mac)
>ncat –C gaia.cs.umass.edu 80 (for Windows)

## Slide 48: Maintaining user/server state: cookies
Recall: HTTP GET/response interaction is stateless
no notion of multi-step exchanges of HTTP messages to complete a Web “transaction”
  no need for client/server to track “state” of multi-step exchange
  all HTTP requests are independent of each other
  no need for client/server to “recover” from a partially-completed-but-never-completely-completed transaction
a stateful protocol: client makes two changes to X, or none at all
time
time
OK
OK
unlock X
OK
update X X’
update X X’’
lock data record X
OK
X
X
X’
X’’
X’’
t’
Q: what happens if network connection or client crashes at t’ ?
Notes: t’

## Slide 49: Maintaining user/server state: cookies
Web sites and client browser use cookies to maintain some state between transactions
four components:
  1) cookie header line of HTTP response message
  2) cookie header line in next HTTP request message
  3) cookie file kept on user’s host, managed by user’s browser
  4) back-end database at Web site
Example:
Susan uses browser on laptop, visits specific e-commerce site for first time
when initial HTTP requests arrives at site, site creates:
  unique ID (aka “cookie”)
  entry in backend database for ID
subsequent HTTP requests from Susan to this site will contain cookie ID value, allowing site to “identify” Susan
Notes: t’

## Slide 50: Maintaining user/server state: cookies
client
Amazon server
usual HTTP response msg
usual HTTP response msg
cookie file
one week later:
usual HTTP request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
usual HTTP request msg
Amazon server
creates ID
1678 for user
create
entry
usual HTTP response
set-cookie: 1678
ebay 8734
amazon 1678
usual HTTP request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
amazon 1678
backend
database
time
time
Notes: t’

## Slide 51: HTTP cookies: comments
What cookies can be used for:
authorization
shopping carts
recommendations
user session state (Web e-mail)
cookies and privacy:
cookies permit sites to learn a lot about you on their site.
third party persistent cookies (tracking cookies) allow common identity (cookie value) to be tracked across multiple web sites
aside
Challenge: How to keep state?
at protocol endpoints: maintain state at sender/receiver over multiple transactions
in messages: cookies in HTTP messages carry state
Notes: t’

## Slide 52
Example: displaying a NY Times web page
nytimes.com
AdX.com
1
HTTP GET
2
HTTP reply
4
3
5
6
NY times page with embedded ad displayed
GET base html file from nytimes.com
1
2
fetch ad from AdX.com
4
5
display composed page
7

## Slide 53
nytimes.com (sports)
AdX.com
1634: sports, 2/15/22
NY Times: 1634
7493: NY Times sports, 2/15/22
HTTP reply
Set cookie: 1634
4
HTTP GET
Referrer: NY Times Sports
5
HTTP reply
Set cookie: 7493
HTTP
GET
AdX: 7493
Cookies: tracking a user’s browsing behavior
“first party” cookie – from website you chose to visit (provides base html file)
“third party” cookie – from website you did not choose to visit

## Slide 54
Cookies: tracking a user’s browsing behavior
nytimes.com
AdX.com
1634: sports, 2/15/22
NY Times: 1634
7493: NY Times sports, 2/15/22
AdX: 7493
socks.com
1
HTTP GET
2
HTTP reply
4
HTTP GET
Referrer: socks.com, cookie: 7493
5
HTTP reply
Set cookie: 7493
7493: socks.com, 2/16/22
AdX:
tracks my web browsing over sites with AdX ads
can return targeted ads based on browsing history

## Slide 55
Cookies: tracking a user’s browsing behavior (one day later)
nytimes.com (arts)
AdX.com
1634: sports, 2/15/22
NY Times: 1634
7493: NY Times sports, 2/15/22
AdX: 7493
socks.com
4
HTTP GET
Referrer: nytimes.com, cookie: 7493
5
HTTP reply
Set cookie: 7493
7493: socks.com, 2/16/22
cookie: 1634
HTTP reply
HTTP
GET
Set cookie: 1634
1634: arts, 2/17/22
7493: NY Times arts, 2/15/22
Returned ad for socks!

## Slide 56
Cookies: tracking a user’s browsing behavior
Cookies can be used to:
track user behavior on a given website (first party cookies)
track user behavior across multiple websites (third party cookies) without user ever choosing to visit tracker site (!)
tracking may be invisible to user:
  rather than displayed ad triggering HTTP GET to tracker, could be an invisible link
third party tracking via cookies:
disabled by default in Firefox, Safari browsers
to be disabled in Chrome browser in 2023

## Slide 57
References
Computer Networking: A Top-Down Approach
  Chapter 2
TCP/IP Protocol Suite
  Chapter 22

## Slide 58
Thank You